## Slide 1: Spoofing a Host: GPS Simulation and Detection
Parveet Kumar • May 2025 • IIT Madras

## Slide 2: Project Overview
• Simulate GPS signal and spoofing attack
• Analyze spoofing power requirements via link budget
• Implement spoofing attack and evaluate impact
• Propose detection model using multi-receiver geometry

## Slide 3: How GPS Works
• GPS uses satellite signals to compute position and time
• Position based on pseudorange:
Rᵢ = ‖L - Lₛᵢ‖ + c·δ
• Requires at least 4 satellites for 3D fix and clock bias

## Slide 4: Vulnerability of Civilian GPS
• Signals are unencrypted and unauthenticated
• Spoofing can override true signal with higher power
• Seamless lock takeover is feasible

## Slide 5: Trilateration Principle
• GPS receiver solves system of equations:
(x - xᵢ)² + (y - yᵢ)² + (z - zᵢ)² = (Rᵢ - Δ)²
• Uses satellite positions and pseudoranges

## Slide 6: Signal Simulation Summary
• ECEF coordinates used for satellites and receiver
• Gaussian noise added to simulate realistic measurements
• Resulting position error within civilian GPS bounds

## Slide 7: Link Budget: Overview
• Used to analyze received signal strength
• Key components: Pt, Gt, Gr, Lfs, Lm
• Determines feasibility of spoofing signal overpowering

## Slide 8: Free Space Path Loss
• Formula: Lfs = 20·log₁₀(d) + 20·log₁₀(f) + 92.45
• Higher distance or lower frequency reduces signal strength

## Slide 9: Link Budget Formula
• Received power:
Pr = Pt + Gt + Gr - Lfs - Lm

## Slide 10: Spoofing Power Requirements
• Spoofer must exceed signal power by 10 dB
• Required power calculated using distance and margins
• Example: ~27 dBW needed from 5 km away

## Slide 11: Spoofing Scenario Setup
• Stationary attacker, moving receiver and fixed target
• Spoofing range: 25 meters
• Trigger spoof when attacker is near receiver

## Slide 12: Spoofing Effect
• Receiver believes it's shifted from true location
• Alters direction toward false target
• Deviation increases over time

## Slide 13: Lock Takeover Constraints
• Relative signal power: ≥ +2 dB
• Time offset < 75 ns
• Location offset < 500 m
• Relative delay mismatch < 80 ns

## Slide 14: Spoofing Detection: Motivation
• GPS receiver alone may not detect seamless spoof
• Lock loss unreliable due to environmental factors

## Slide 15: Proposed Detection Model
• Use multiple GPS receivers in known formation
• Detect geometry distortion during spoof
• Preserve mutual distance and time constraints

## Slide 16: Group Spoofing Constraints
• Must maintain pseudorange differences:
|Pj - Pk| ≥ |L'j - L'k| + Δj - Δk
• Violations indicate spoofing attempt

## Slide 17: Geometry-based Detection
• Spoofing many receivers limits attacker positions
• ≥4 receivers reduce spoofing options to 1–2 positions
• Can verify consistency of computed positions

## Slide 18: Summary of Results
• Single receiver easily spoofed
• Multiple receivers restrict spoof precision
• Precise alignment in time and location is critical

## Slide 19: Conclusion
• GPS spoofing is feasible with civilian signals
• Power margin and timing alignment are essential
• Multi-receiver detection offers robust defense

## Slide 20: Future Work
• Hardware implementation with SDR
• Integration with ML-based anomaly detectors
• Deployment in vehicular or drone platforms